## Slide 1: Single-Cycle/Non-Pipelined Datapath (Modify to Support 16 Instructions)
Instr[25-0]
26
Shift
left 2
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
BT
1
1
1
0
0
0
0
1
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15-11]
Control
Unit
Instr[31-26]
0
1
32
PC+4[31-28]
28
J
ALUControl
Instr[5-0]
BEQ
RegDst
BNE
JR
1
0
$31
0
1
JAL
0
1
Notes: For lecture
Good exam questions
Add jalr rs,rd 0 rs 0 rd 0 9
jump to instr whose addr is in rs and save addr of next inst (PC+4) in rd
Add the PowerPC addressing modes of update addressing and indexed addressing (will have to expand the RegFile to be three read port and two write port)
Add andi, ori, addi - have to have both a signextend and a zeroextend and choose between the two, will have to augment the ALUop encoding (since can’t get the op information out of the funct bits as with R-type)
Add mult rs, rt with the result being left in hi|lo - so also include the mfhi and mflo instructions (will have to add a multiplier, the hi and lo registers and then a couple of muxes and their control).
Add barrel shifter

## Slide 2: Extended ALU Control (Use This Table to Complete the CU Table)
ALUControl derived from opcode and funct
  Combinational logic derives ALU control
opcode
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6

## Slide 3: Extended Control Unit (Modify to Support 16 Instructions)
opcode | funct | ALUControl | RegDst | ALUSrc | MemToReg | RegWr | MemWr | BEQ | J | BNE | Jal | Jr
R-type ≡ 000000 | AND 100100 | 0000 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
 | OR 100101 | 0001 |  |  |  |  |  |  |  |  |  | 
 | add 100000 | 0010 |  |  |  |  |  |  |  |  |  | 
 | sub 100010 | 0110 |  |  |  |  |  |  |  |  |  | 
 | slt 101010 | 0111 |  |  |  |  |  |  |  |  |  | 
 | NOR 100111 | 1100 |  |  |  |  |  |  |  |  |  | 
 | jr 001000 | 0000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
lw ≡ 100011 | xxxxxx | 0010 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
sw ≡ 101011 | xxxxxx | 0010 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
beq ≡ 000100 | xxxxxx | 0110 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
j ≡ 000010 | xxxxxx | 0000 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
addi ≡ 001000 | xxxxxx | 0010 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
bne ≡ 000101 | xxxxxx | 0110 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
jal ≡ 000011 | xxxxxx | 0000 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
ori ≡ 001101 | xxxxxx | 1101 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
lui ≡ 001111 | xxxxxx | 1111 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Notes: For class handout